Crane Operation Daily Checklist Plant#___________ I.D.#____________ Location:_____________ Make:___________ Model#___________ Type:____________ Volts:_____________ Supv:___________ Month___________ Item Number The following applicable items shall be checked daily, other items may apply. Date 1 2 3 4 5 6 7 8 Operator 1.) Test run unit, observe operation for malfunctions -safety, emergency stop -pendant, joystick -correct direction of motions -brakes of all motions 2.) Check for deteriorations or leakage in lines, tanks, valves, drain pumps and other parts of air or hydraulic systems 3.) Examine load hooks for wear, cracks, or damage-saddle wear (10%) -twist (10%) -throat opening (15%) 4.) Check Hoist Rope, or Chain-end connections Chain- excessive wear, twist distorted links, stretch Rope- crushing, kinking, broken wires -latch 5.) Check load attachments-capacity ratings, end connections Chain- excessive wear, twist, distorted links, stretch Slings- crushing, kinking, broken wires tears 6.) Check for excessive wear, cracks or components-hook block, sheaves, hook 7.) Check all running ropes and chains for correct reeving-proper spooling 8.) Check upper limit with no load 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31 Operators Condition Code: A=Acceptable D=Defective, Report at Once Date Condition Signature 1.) Hook 2.) Hoist Rope or Chain Inspector Comments:

Integrity Crane Services, Ltd  330-834-2000