Wire Rope 101

|  | A wire rope is a piece of flexible, multiwired, stranded machinery made of many precision parts. IWRC (independent Wire Rope Core) provides good crush resistance and increased strength. Fiber Core provides excellent flexibility Usually a wire rope consists of a core member, around which a number of multiwired strands are "laid" or helically bent. There are two general types of cores for wire rope fiber cores and wire cores. The fiber core may be made from natural or synthetic fibers. The wire core can be an Independent Wire Rope Core (IWRC), or a Strand Core (SC). The purpose of the core is to provide support and maintain the position of the outer strands during operation. Any number of multiwired strands may be laid around the core. The most popular arrangement is six strands around the core, as this combination gives the best balance. The number of wires per strand may vary from 3 to 91, with the majority of wire ropes falling into the 7-wire, 19-wire, or 37-wire strand categories. Understand what the "lays" of wire rope mean "Lay" of a wire rope is simply a description of the way wires and strands are placed during construction. Right lay and left lay refers to the direction of strands. Right lay means that the strands pass from left to right across the rope. Left lay means just the opposite: strands pass from right to left. Regular lay and lang lay describes the way wires are placed within each strand. Regular lay means that wire in the strands are laid opposite in direction to the lay of the strands. Lang lay means that wires are laid in the same direction as the lay of the strands. Most of the wire rope used is right lay, regular lay. This specification has the widest range of applications and meets the requirements of most equipment. In fact, other lay specifications are considered exceptions and must be requested when ordering. Here are some exceptions Lang lay is recommended for much excavating, construction, and mining applications, including draglines, hoist lines, dredgelines and other similar lines. Here's why. Lang lay ropes are more flexible than regular lay ropes. They also have greater wearing surface per wire than regular lay ropes. Where properly recommended, installed and used, lang lay ropes can be used to greater advantage than regular lay ropes. However, lang lay ropes are more susceptible to the abuses of bending over small diameter sheaves, pinching in undersize sheave grooves, crushing when winding on drums, and failing due to excessive rotation. Left lay rope has greatest usage in oil fields on rod and tubing lines, blast hole rigs, and spudders where rotation of right lay rope would loosen couplings. The rotation of a left lay rope tightens a standard coupling. |
| --- | --- |

| Lay | Definition | Characteristics |
| --- | --- | --- |
|  | Most common lay in which the wires wind in one direction and the strands the opposite direction. (right lay shown) | Less likely to kink and untwist; easier to handle; more crush resistant than lang lay. |
|  | Wires in strand and strands of rope wind the same direction. (right lay shown) | Increased resistance to abrasion; greater flexibility and fatigue resistance than regular lay; will kink and untwist. |
|  | Strands wound to the right around the core. (regular lay shown) | The most common construction |
|  | Strands wound to the left around the core. (regular lay shown) | Used in a few special situations - cable tool drilling line, for example. |
|  | Alternate strands of right regular lay and right lang lay. | Combines the best features of regular and lang lay for boom hoist or winch lines. |

|  | 6x7 Rope - Excellent abrasion resistance; less bending fatigue resistance. Dragging and haulage in mines, inclined planes and tramways, sand lines. |
| --- | --- |

|  | 6 x 19 - Seale Characteristics Resistant to abrasion and crushing; medium fatigue resistance Typical Applications Haulage rope, choker rope, rotary drilling line IWRC shown; fiber core available |  | 6x2l Filler Wire Characteristics Less abrasion resistance; more bending fatigue resistance Typical Applications Pull Ropes, load lines, backhaul ropes, draglines IWRC shown; fiber core available |
| --- | --- | --- | --- |
|  | 6x25 Filler Wire Characteristics Most flexible rope in classification; best balance of abrasion and fatigue resistance Typical Applications Most widely used of all wire ropes - cranes hoists, skip hoists, haulage, mooring lines, conveyors, etc. IWRC shown fiber core available |  | 6x26 Warrington Seale Characteristics Good balance of abrasion and fatigue resistance Typical Applications Boom hoists, logging and tubing lines IWRC shown, fiber core available |

| Core | Characteristics | Typical Applications |
| --- | --- | --- |
|  | 6 x 31 Warrington Seale 12 outside wires. Slightly more flexible than 6 x 25 rope with the same abrasion resistance IWRC shown, fiber core available | Overhead crane and mobile crane hoist ropes |
|  | 6 x 36 Warrington Seale 14 outside wires. More fatigue resistance; but less abrasion resistance than 6 x 25 rope. IWRC shown; fiber core available | Overhead crane and mobile crane hoist ropes; winch lines; large diameter towing lines |
|  | 6 x 41 Warrington Seale 16 outside wires. Good combination of fatigue and abrasion resistance for operating ropes 1WRC shown, fiber core available | Overhead crane and mobile crane hoist ropes; shovel and dragline hoist ropes |
|  | 6 x 41 Seale Filler Wire Same characteristics and applications as 6 x 41 Warrington Seale IWRC shown, fiber core available | Overhead crane and mobile crane hoist ropes; shovel and dragline hoist ropes |
|  | 6 x 49 Seale Warrington Seale 16 outside wires. Best fatigue resistance and abrasion resistance in 6 x 37 classification lWRC shown; fiber core available | Mooring, towing and anchor lines |